## Slide 1: CS162 Operating Systems and Systems Programming Lecture 26 Networking and TCP/IP (Con’t), DNS, RPC, Distributed File Systems
April 25th, 2023
Prof. John Kubiatowicz
http://cs162.eecs.Berkeley.edu

## Slide 2: Recall: Distributed Consensus Making
Consensus problem
  All nodes propose a value
  Some nodes might crash and stop responding
  Eventually, all remaining nodes decide on the same value from set of proposed values
Distributed Decision Making
  Choose between “true” and “false”
  Or Choose between “commit” and “abort”
Equally important (but often forgotten!): make it durable!
  How do we make sure that decisions cannot be forgotten?
    This is the “D” of “ACID” in a regular database
  In a global-scale system?
    What about erasure coding or massive replication?
    Like BlockChain applications!

## Slide 3: Recall: Wide Area Network
Wide Area Network (WAN): network that covers a broad area (e.g., city, state, country, entire world)
  E.g., Internet is a WAN
WAN connects multiple Local Area Networks (LANs)
Datalink layer networks are connected by routers
  Different LANs can use different communication technology (e.g., wireless, cellular, optics, wired)
Host A
(IP A)
Host B
(IP B)
R2
R3
R4
R1
LAN
LAN
LAN

## Slide 4: Recall: Routers
Forward each packet received on an incoming link to an outgoing link based on packet’s destination IP address (towards its destination)
Store & forward: packets are buffered before being forwarded
Forwarding table: mapping between IP address and the output link
incoming links
outgoing links
Router
Memory

## Slide 5: Recall: Packet Forwarding
Upon receiving a packet, a router
  read the IP destination address of the packet
  consults its forwarding table  output port
  forwards packet to corresponding output port
Default route (for subnets without explicit entries)
  Forward to more authoritative router
Host A
(IP A)
Host B
(IP B)
R2
R3
R4
R1
IP B
LAN
LAN
LAN

## Slide 6: Setting up Routing Tables
How do you set up routing tables?
  Internet has no centralized state!
    No single machine knows entire topology
    Topology constantly changing (faults, reconfiguration, etc.)
  Need dynamic algorithm that acquires routing tables
    Ideally, have one entry per subnet or portion of address
    Could have “default” routes that send packets for unknown subnets to a different router that has more information
Possible algorithm for acquiring routing table
  Routing table has “cost” for each entry
    Includes number of hops to destination, congestion, etc.
    Entries for unknown subnets have infinite cost
  Neighbors periodically exchange routing tables
    If neighbor knows cheaper route to a subnet, replace your entry with neighbors entry (+1 for hop to neighbor)
In reality:
  Internet has networks of many different scales
  Different algorithms run at different scales (e.g. BGP globally, OSPF locally,…)

## Slide 7: Naming in the Internet
How to map human-readable names to IP addresses?
  E.g. www.berkeley.edu  128.32.139.48
  E.g. www.google.com  different addresses depending on location, and load
Why is this necessary?
  IP addresses are hard to remember
  IP addresses change:
    Say, Server 1 crashes gets replaced by Server 2
    Or – google.com handled by different servers
Mechanism: Domain Naming System (DNS)
Name
Address


## Slide 8: Domain Name System
DNS is a hierarchical mechanism for naming
  Name divided in domains, right to left: www.eecs.berkeley.edu
Each domain owned by a particular organization
  Top level handled by ICANN (Internet Corporation for Assigned Numbers and Names)
  Subsequent levels owned by organizations
Resolution: series of queries to successive servers
Caching: queries take time, so results cached for period of time
Top-level
com
edu
Mit.edu
169.229.131.81
128.32.61.103
128.32.139.48
berkeley.edu
www
calmail
eecs
berkeley
MIT
eecs.berkeley.edu
www

## Slide 9: How Important is Correct Resolution?
If attacker manages to give incorrect mapping:
  Can get someone to route to server, thinking that they are routing to a different server
    Get them to log into “bank” – give up username and password
Is DNS Secure?
  Definitely a weak link
    What if “response” returned from different server than original query?
    Get person to use incorrect IP address!
  Attempt to avoid substitution attacks:
    Query includes random number which must be returned
In July 2008, hole in DNS security located!
  Dan Kaminsky (security researcher) discovered an attack that broke DNS globally
    One person in an ISP convinced to load particular web page, then all users of that ISP end up pointing at wrong address
  High profile, highly advertised need for patching DNS
    Big press release, lots of mystery
    Security researchers told no speculation until patches applied

## Slide 10: Network Layering
Layering: building complex services from simpler ones
  Each layer provides services needed by higher layers by utilizing services provided by lower layers
The physical/link layer is pretty limited
  Packets are of limited size (called the “Maximum Transfer Unit or MTU: often 200-1500 bytes in size)
  Routing is limited to within a physical link (wire) or perhaps through a switch
Our goal in the following is to show how to construct a secure, ordered, message service routed to anywhere:
Physical Reality: Packets | Abstraction: Messages
Limited Size (MTU) | Arbitrary Size
Unordered (sometimes) | Ordered
Unreliable | Reliable
Machine-to-machine | Process-to-process
Only on local area net | Routed anywhere
Asynchronous | Synchronous
Insecure | Secure

## Slide 11: Building a messaging service
Handling Arbitrary Sized Messages:
  Must deal with limited physical packet size
  Split big message into smaller ones (called fragments)
    Must be reassembled at destination
  Checksum computed on each fragment or whole message
Internet Protocol (IP): Provides way to send datagrams to arbitrary destination
  Deliver messages unreliably (“best effort”) from one machine in Internet to another
  Since intermediate links may have limited size, must be able to fragment/reassemble packets on demand
  Includes 256 different “sub-protocols” build on top of IP
    Examples: ICMP(1), TCP(6), UDP (17), IPSEC(50,51)

## Slide 12: Recall: IPv4 Packet Format
IP Packet Format:
IP Datagram: an unreliable, unordered, packet sent from source to destination
  Function of network – deliver datagrams!
16-bit identification
ToS
4
13-bit frag off
Total length(16-bits)
protocol
TTL
16-bit header checksum
32-bit source IP address
32-bit destination IP address
IHL
flags
options (if any)
Data
0
15
16
31
IP Ver4
IP Header
Length
Size of datagram
(header+data)
Flags &
Fragmentation
to split large
messages
Time to
Live (hops)
Type of
transport
protocol
IP header
20 bytes

## Slide 13: Building a messaging service on IP
Process to process communication
  Basic routing gets packets from machinemachine
  What we really want is routing from processprocess
    Add “ports”, which are 16-bit identifiers
    A communication channel (connection) defined by 5 items: [source addr, source port, dest addr, dest port, protocol]
For example: The Unreliable Datagram Protocol (UDP)
  Layered on top of basic IP (IP Protocol 17)
  Datagram: an unreliable, unordered, packet sent from source user  dest user (Call it UDP/IP)
  Important aspect: low overhead!
    Often used for high-bandwidth video streams
    Many uses of UDP considered “anti-social” – none of the “well-behaved” aspects of (say) TCP/IP
UDP Data
16-bit UDP length
16-bit UDP checksum
16-bit source port
16-bit destination port
IP Header
(20 bytes)

## Slide 14: Administrivia
Midterm 3: This Thursday!
  No class on Thursday. I’ll have special office hours during class time.
  Three double-sided pages of notes
  Watch for Ed post about where you should go: we have multiple exam rooms
All material up to today’s lecture is fair game
Final deadlines during RRR week:
  Yes, there will be office hour – watch for specifics
Also – we have a special lecture (just for fun) next Tuesday
  During normal class time!

## Slide 15: Administrivia (Con’t)
You need to know your units as CS/Engineering students!
Units of Time: “s”: Second, “min”: 60s, “h”: 3600s, (of course)
  Millisecond: 1ms  10-3 s
  Microsecond: 1s  10-6 s
  Nanosecond: 1ns:  10-9 s
  Picosecond: 1ps  10-12 s
Integer Sizes: “b”  ”bit”, “B”  “byte” == 8 bits, “W””word”==? (depends. Could be 16b, 32b, 64b)
Units of Space (memory), sometimes called the “binary system”
  Kilo: 1KB  1KiB  1024 bytes == 210 bytes == 1024  1.0×103
  Mega: 1MB  1MiB  (1024)2 bytes == 220 bytes == 1,048,576  1.0×106
  Giga: 1GB  1GiB  (1024)3 bytes == 230 bytes == 1,073,741,824  1.1×109
  Tera: 1TB  1TiB  (1024)4 bytes == 240 bytes == 1,099,511,627,776  1.1×1012
  Peta: 1PB  1PiB  (1024)5 bytes == 250 bytes == 1,125,899,906,842,624  1.1 × 1015
  Exa: 1EB  1EiB  (1024)6 bytes == 260 bytes == 1,152,921,504,606,846,976  1.2 × 1018
Units of Bandwidth, Space on disk/etc, Everything else…, sometimes called the “decimal system”
  Kilo: 1KB/s  103 bytes/s, 1KB  103 bytes
  Mega: 1MB/s 106 bytes/s, 1MB  106 bytes
  Giga: 1GB/s  109 bytes/s, 1GB  109 bytes
  Tera: 1TB/s  1012 bytes/s, 1TB  1012 bytes
  Peta: 1PB/s  1015 bytes/s, 1PB  1015 bytes
  Exa: 1EB/s  1018 bytes/s, 1EB  1018 bytes

## Slide 16: Internet Architecture: Five Layers
Lower three layers implemented everywhere
Top two layers implemented only at hosts
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router
sockets
sockets

## Slide 17: Internet Architecture: Five Layers
Communication goes down to physical network
Then from network peer to peer
Then up to relevant layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router
sockets
sockets

## Slide 18: Layering Analogy: Packets in Envelopes
101010100110101110
Physical Layer
Physical Layer
101010100110101110
Datalink Layer
Trans.
Hdr.
Net.
Hdr.
Frame
Hdr.
Datalink Layer
Trans.
Hdr.
Net.
Hdr.
Frame
Hdr.
Data
Data
Network Layer
Trans.
Hdr.
Net.
Hdr.
Network Layer
Trans.
Hdr.
Net.
Hdr.
Data
Data
Transport Layer
Trans.
Hdr.
Transport Layer
Trans.
Hdr.
Data
Data
Data
Application Layer
Application Layer
Data
Transport
Network
Datalink
Physical
Session
Present.
Application

## Slide 19: Internet Transport Protocols
Datagram service (UDP): IP Protocol 17
  No-frills extension of “best-effort” IP
  Multiplexing/Demultiplexing among processes
Reliable, in-order delivery (TCP): IP Protocol 6
  Connection set-up & tear-down
  Discarding corrupted packets (segments)
  Retransmission of lost packets (segments)
  Flow control/Congestion control
Other examples:
  DCCP (33), Datagram Congestion Control Protocol
  RDP (26), Reliable Data Protocol
  SCTP (132), Stream Control Transmission Protocol
Transport
Network
Datalink
Physical
Session
Present.
Application

## Slide 20: Network Address Translation: Transport-Level IP Sharing
Server #2 External IP: 11.33.40.5
Server #1 External IP: 142.251.42.36
Public Internet
Client #2 Internal IP: 192.168.1.10
Client #1 Internal IP: 192.168.1.4
Private Network
(192.168.xx.xx)
Firewall
External IP: 128.32.5.3
Network Address Translation (NAT): Allow multiple clients to share Public IP
  Translate connections with Private IP addresses to Public IP Address (of firewall)
Allocate unique (client) port at firewall to distinguish different connections
TCP Connection #1: [192.168.1.4, Port: 6543, 142.251.42.36, Port: 80 ]
TCP Connection #1: [128.32.5.3, Port: 4340, 142.251.42.36, Port: 80 ]
TCP Connection #2: [192.168.1.4, Port: 8977, 11.33.40.5, Port: 80 ]
TCP Connection #2: [128.32.5.3, Port: 4341, 11.33.40.5, Port: 80 ]

## Slide 21: Recall: Sockets in concept
Client
Server
read response
Close Client Socket
Create Client Socket
Connect it to server (host:port)
Create Server Socket
Bind it to an Address
(host:port)
Listen for Connection
Close Connection Socket
Close Server Socket
write request
write response
Accept syscall()
Connection Socket
Connection Socket
read request

## Slide 22: Reliable Message Delivery: the Problem
All physical networks can garble and/or drop packets
  Physical media: packet not transmitted/received
    If transmit close to maximum rate, get more throughput – even if some packets get lost
    If transmit at lowest voltage such that error correction just starts correcting errors, get best power/bit
  Congestion: no place to put incoming packet
    Point-to-point network: insufficient queue at switch/router
    Broadcast link: two host try to use same link
    In any network: insufficient buffer space at destination
    Rate mismatch: what if sender send faster than receiver can process?
Reliable Message Delivery on top of Unreliable Packets
  Need some way to make sure that packets actually make it to receiver
    Every packet received at least once
    Every packet received at most once
  Can combine with ordering: every packet received by process at destination exactly once and in order

## Slide 23: Transmission Control Protocol (TCP)
Transmission Control Protocol (TCP)
  TCP (IP Protocol 6) layered on top of IP
  Reliable byte stream between two processes on different machines over Internet (read, write, flush)
TCP Details
  Fragments byte stream into packets, hands packets to IP
    IP may also fragment by itself
  Uses window-based acknowledgement protocol (to minimize state at sender and receiver)
    “Window” reflects storage at receiver – sender shouldn’t overrun receiver’s buffer space
    Also, window should reflect speed/capacity of network – sender shouldn’t overload network
  Automatically retransmits lost packets
  Adjusts rate of transmission to avoid congestion
    A “good citizen”
Router
Router
Stream in:
Stream out:
..zyxwvuts
gfedcba

## Slide 24: Problem: Dropped Packets
All physical networks can garble or drop packets
  Physical hardware problems (bad wire, bad signal)
Therefore, IP can garble or drop packets
  It doesn't repair this itself (end-to-end principle!)
Building reliable message delivery
  Confirm that packets aren't garbled
  Confirm that packets arrive exactly once

## Slide 25: Using Acknowledgements
How to ensure transmission of packets?
  Detect garbling at receiver via checksum, discard if bad
  Receiver acknowledges (by sending “ACK”) when packet received properly at destination
  Timeout at sender: if no ACK, retransmit
Some questions:
  If the sender doesn’t get an ACK, does that mean the receiver didn’t get the original message?
    No
  What if ACK gets dropped? Or if message gets delayed?
    Sender doesn’t get ACK, retransmits, Receiver gets message twice, ACK each
B
A
Packet
ACK
B
A
Packet
ACK
Packet
Timeout
Notes: - So how can we ensure delivery of packets over an unreliable network?

## Slide 26: Stop-and-Wait (No Packet Loss)
Send; wait for ACK; repeat
Round Trip Time (): time it takes a packet to travel from sender to receiver and back
  One-way latency (): one way delay from sender and receiver
For symmetric latency,
ACK 1
Time
Sender
Receiver
1
2
ACK 2
3
RTT
RTT
d

## Slide 27: Stop-and-Wait (No Packet Loss)
How fast can you send data?
Little’s Law applied to the network:
For Stop-and-Wait, packet
So bandwidth is 1 packet per RTT
  Depends only on latency, not network capacity (!)
ACK 1
Time
Sender
Receiver
1
2
ACK 2
3
RTT
RTT
d

## Slide 28: Stop-and-Wait (No Packet Loss)
So bandwidth is 1 packet per RTT
  Depends only on latency, not network capacity (!)
Suppose RTT = 100 ms and 1 packet is 1500 Bytes
Throughput = = 120 Kbps
Very inefficient if we have a 100 Mbps link!
ACK 1
Time
Sender
Receiver
1
2
ACK 2
3
RTT
RTT
d

## Slide 29: Stop-and-Wait with Packet Loss
Loss recovery relies on timeouts
How to choose a good timeout?
  Too short – lots of duplication
  Too long – packet loss is really disruptive!
How to deal with duplication?
  Retransmission certainly opens up the possibility for copies of packets
ACK 1
Time
Sender
Receiver
1
RTT
timeout
1

## Slide 30: How to Deal with Message Duplication?
Solution: put sequence number in message to identify re-transmitted packets
  Receiver checks for duplicate number’s; Discard if detected
Requirements:
  Sender keeps copy of unACK’d messages
    Easy: only need to buffer small number of messages
  Receiver tracks possible duplicate messages
    Hard: when ok to forget about received message?
Alternating-bit protocol:
  Send one message at a time; don’t send next message until ACK received
  Sender keeps last message; receiver tracks sequence number of last message received
Pros: simple, small overhead
Con: doesn’t work if network can delay or duplicate messages arbitrarily
Pkt #0
ACK #0
Pkt #1
ACK #1
Pkt #0
ACK #0
Sender
Receiver

## Slide 31: Advantages of Moving Away From Stop-and-Wait
Larger space of acknowledgements
  Pipelining: don’t wait for ACK before sending next packet
ACKs serve dual purpose:
  Reliability: Confirming packet received
  Ordering: Packets can be reordered at destination
How much data is in flight now?
  Bytes in-flight: Wsend = RTT × B
  Here B is in “bytes/second”
  Wsend  Sender’s “Window Size”
  Packets in flight = (Wsend / packet size)
How long does the sender have to keep the packets around?
How long does the receiver have to keep the packets’ data?
What if sender is sending packets faster than the receiver can process the data?
Time
Sender
Receiver
RTT
d

## Slide 32: Recall: Communication Between Processes
Data written by A is held in memory until B reads it
Queue has a fixed capacity
  Writing to the queue blocks if the queue if full
  Reading from the queue blocks if the queue is empty
POSIX provides this abstraction in the form of pipes
write(wfd, wbuf, wlen);
n = read(rfd,rbuf, rmax);
Process A
Process B
In-Memory Queue

## Slide 33: Buffering in a TCP Connection
Host 1
A single TCP connection needs four in-memory queues:
  Send buffer: add data on write syscall, remove data when ACK received
  Receive buffer: add data when packets received, remove data on read syscall
Process A
Send Queue
Receive Queue
Host 2
Process B
Receive Queue
Send Queue
Separate pair of queues per TCP connection
Data (Packets)
Data (Packets)

## Slide 34: Window Size: Space in Receive Queue
Host 1
A host’s window size for a TCP connection is how much remaining space it has in its receive queue
A host advertises its window size in every TCP packet it sends!
Sender never sends more than receiver’s advertised window size
Process A
Send Queue
Receive Queue
Host 2
Process B
Receive Queue
Send Queue
Separate pair of queues per TCP connection
Data (Packets)
Data (Packets)

## Slide 35: Sliding Window Protocol
TCP sender knows receiver’s window size, and aims never to exceed it
But packets that it previously send may arrive, filling the window size!
Rule: TCP sender ensures that:
Number of Sent but UnACKed Bytes < Receiver’s Advertised Window Size
Can send new packets as long as sent-but-unacked packets haven’t already filled the advertised window size

## Slide 36: Sliding Window (No Packet Loss)
Example:Window size () = 3 packets
Window size to fill link is given by:
Bpkt  Packets/sec
Little’s Law once again!
For TCP, window is in bytes, not packets
Time
Sender
Receiver
1
{1}
2
{1, 2}
3
{1, 2, 3}
4
{2, 3, 4}
5
{3, 4, 5}
Unacked packets that sender sent
Out-of-seq packets
in receiver’s window
{}
6
{4, 5, 6}
.
.
.
.
.
.
{}
{}

## Slide 37: TCP Windows and Sequence Numbers: PER BYTE!
Sender has three regions:
  Sequence regions
    sent and ACK’d
    sent and not ACK’d
    not yet sent
  Window (colored region) adjusted by sender
Receiver has three regions:
  Sequence regions
    received and ACK’d (given to application)
    received and buffered
    not yet received (or discarded because out of order)
Sequence Numbers
Sent
not ACK’d
Sent
ACK’d
Not yet
sent
Sender
Not yet
received
Received
Given to app
Received
Buffered
Receiver

## Slide 38: Window-Based Acknowledgements (TCP)
Seq:190
Size:40
Seq:230
A:190/210
Seq:260
A:190/210
Seq:300
A:190/210
Seq:190
A:340/60
Seq:340
A:380/20
Seq:380
A:400/0
A:100/300
Seq:100
A:140/260
Seq:140
A:190/210
100
Seq:100
Size:40
140
Seq:140
Size:50
190
Seq:230
Size:30
230
260
Seq:260
Size:40
300
Seq:300
Size:40
340
Seq:340
Size:40
380
Seq:380
Size:20
400
Retransmit!

## Slide 39: Congestion
Too much data trying to flow through some part of the network
IP’s solution: Drop packets
What happens to TCP connection?
  Lots of retransmission – wasted work and wasted bandwidth (when bandwidth is scarce)

## Slide 40: Congestion Avoidance
Congestion
  How long should timeout be for re-sending messages?
    Too long  wastes time if message lost
    Too short  retransmit even though ACK will arrive shortly
  Stability problem: more congestion  ACK is delayed  unnecessary timeout  more traffic  more congestion
    Closely related to window size at sender: too big means putting too much data into network
How does the sender’s window size get chosen?
  Must be less than receiver’s advertised buffer size
  Try to match the rate of sending packets with the rate that the slowest link can accommodate
  Sender uses an adaptive algorithm to decide size of N
    Goal: fill network between sender and receiver
    Basic technique: slowly increase size of window until acknowledgements start being delayed/lost
TCP solution: “slow start” (start sending slowly)
  If no timeout, slowly increase window size (throughput) by 1 for each ACK received
  Timeout  congestion, so cut window size in half
  “Additive Increase, Multiplicative Decrease”
Notes: 2nd thing we use window-based acknowledgment protocol for:
Avoid overwhelming network

## Slide 41: Congestion Management
TCP artificially restricts the window size if it sees packet loss
Careful control loop to make sure:
  We don’t send too fast and overwhelm the network
  We utilize most of the bandwidth the network has available
  In general, these are conflicting goals!

## Slide 42: Recall: Connection Setup over TCP/IP
5-Tuple identifies each connection:
  Source IP Address
  Destination IP Address
  Source Port Number
  Destination Port Number
  Protocol (always TCP here)
socket
Request Connection
Server
Client
Server
Socket
new
socket
Connection
socket
connection
Often, Client Port “randomly” assigned
  Done by OS during client socket setup
Server Port often “well known”
  80 (web), 443 (secure web), 25 (sendmail), etc
  Well-known ports from 0—1023

## Slide 43: Establishing TCP Service
Open connection: 3-way handshaking
  Need to establish bidirectional communication, including sequence numbers
Reliable byte stream transfer from (IPa, TCP_Port1) to (IPb, TCP_Port2)
  Indication if connection fails: Reset
Close (tear-down) connection

## Slide 44: Sockets in concept
Client
Server
read response
Close Client Socket
Create Client Socket
Connect it to server (host:port)
Create Server Socket
Bind it to an Address
(host:port)
Listen for Connection
Close Connection Socket
Close Server Socket
write request
write response
Accept syscall()
Connection Socket
Connection Socket
read request

## Slide 45: Open Connection: 3-Way Handshake
Server calls listen() to wait for a new connection
Client calls connect() providing server’s IP address and port number
Each side sends SYN packet proposing an initial sequence number (one for each sender) and ACKs the other
Client (initiator)
SYN, SeqNum = x
SYN and ACK, SeqNum = y and Ack = x + 1
ACK, Ack = y + 1
connect()
listen()
accept() dequeues connection
allocate buffer space,
connection enqueued
time
Server

## Slide 46: Sockets in concept
Client
Server
read response
Close Client Socket
Create Client Socket
Connect it to server (host:port)
Create Server Socket
Bind it to an Address
(host:port)
Listen for Connection
Close Connection Socket
Close Server Socket
write request
write response
Accept syscall()
Connection Socket
Connection Socket
read request

## Slide 47: Close Connection: 4-Way Teardown
Connection is not closed until both sides agree
FIN
FIN ACK
FIN
FIN ACK
Host 1
Host 2
Can retransmit FIN ACK if it is lost
timeout
OS deallocates connection state
close()
close()
OS deallocates connection state
data
OS discards data (no socket to give it to)
Any calls to read() return 0
If multiple FDs on Host 1 refer to this connection, all of them must be closed
Same for close() call on Host 2

## Slide 48: Recall: Distributed Applications Build With Messages
How do you actually program a distributed application?
  Need to synchronize multiple threads, running on different machines
    No shared memory, so cannot use test&set
  One Abstraction: send/receive messages
    Already atomic: no receiver gets portion of a message and two receivers cannot get same message
Interface:
  Mailbox (mbox): temporary holding area for messages
    Includes both destination location and queue
  Send(message,mbox)
    Send message to remote mailbox identified by mbox
  Receive(buffer,mbox)
    Wait until mbox has message, copy into buffer, and return
    If threads sleeping on this mbox, wake up one of them
Network
Send
Receive

## Slide 49: Question: Data Representation
An object in memory has a machine-specific binary representation
  Threads within a single process have the same view of what’s in memory
  Easy to compute offsets into fields, follow pointers, etc.
In the absence of shared memory, externalizing an object requires us to turn it into a sequential sequence of bytes
  Serialization/Marshalling: Express an object as a sequence of bytes
  Deserialization/Unmarshalling: Reconstructing the original object from its marshalled form at destination

## Slide 50: Simple Data Types
uint32_t x;
Suppose I want to write a x to a file
First, open the file: FILE* f = fopen(“foo.txt”, “w”);
Then, I have two choices:
  fprintf(f, “%lu”, x);
  fwrite(&x, sizeof(uint32_t), 1, f);
    Or equivalently, write(fd, &x, sizeof(uint32_t)); (perhaps with a loop to be safe)
Neither one is “wrong” but sender and receiver should be consistent!

## Slide 51: Machine Representation
Consider using the machine representation:
  fwrite(&x, sizeof(uint32_t), 1, f);
How do we know if the recipient represents x in the same way?
  For pipes, is this a problem?
  What about for sockets?

## Slide 52: Endianness
For a byte-address machine, which end of a machine-recognized object (e.g., int) does its byte-address refer to?
Big Endian: address is the most-significant bits
Little Endian: address is the least-significant bits

## Slide 53: What Endian is the Internet?
Big Endian
  Network byte order
  Vs. “host byte order”

## Slide 54: Dealing with Endianness
Decide on an “on-wire” endianness
Convert from native endianness to “on-wire” endianness before sending out data (serialization/marshalling)
  uint32_t htonl(uint32_t) and uint16_t htons(uint16_t) convert from native endianness to network endianness (big endian)
Convert from “on-wire” endianness to native endianness when receiving data (deserialization/unmarshalling)
  uint32_t ntohl(uint32_t) and uint16_t ntohs(uint16_t) convert from network endianness to native endianness (big endian)

## Slide 55: What About Richer Objects?
Consider word_count_t of Homework 0 and 1 …
Each element contains:
  An int
  A pointer to a string (of some length)
  A pointer to the next element
fprintf_words writes these as a sequence of lines (character strings with \n) to a file stream
What if you wanted to write the whole list as a binary object (and read it back as one)?
  How do you represent the string?
  Does it make any sense to write the pointer?

## Slide 56: Data Serialization Formats
JSON and XML are commonly used in web applications
Lots of ad-hoc formats

## Slide 57: Data Serialization Formats

## Slide 58: Remote Procedure Call (RPC)
Raw messaging is a bit too low-level for programming
  Must wrap up information into message at source
  Must decide what to do with message at destination
  May need to sit and wait for multiple messages to arrive
  And must deal with machine representation by hand
Another option: Remote Procedure Call (RPC)
  Calls a procedure on a remote machine
  Idea: Make communication look like an ordinary function call
  Automate all of the complexity of translating between representations
  Client calls: remoteFileSystemRead("rutabaga");
  Translated automatically into call on server: fileSysRead("rutabaga");

## Slide 59: RPC Concept
Client (caller)
r = f(v1, v2);
Server (callee)
res_t f(a1, a2)
call
return
receive
return
call
Client
Stub
bundle
args
bundle
ret vals
unbundle
ret vals
send
receive
send
Server
Stub
unbundle
args

## Slide 60: RPC Information Flow
Client (caller)
r = f(v1, v2);
Server (callee)
res_t f(a1, a2)
call
return
receive
return
call
bundle
ret vals
unbundle
ret vals
send
receive
Machine A
Machine B
Packet
Handler
Packet
Handler
Network
Network
Server
Stub
unbundle
args
send
Server
Stub
unbundle
args
Client
Stub
bundle
args

## Slide 61: RPC Implementation
Request-response message passing (under covers!)
“Stub” provides glue on client/server
  Client stub is responsible for “marshalling” arguments and “unmarshalling” the return values
  Server-side stub is responsible for “unmarshalling” arguments and “marshalling” the return values.
Marshalling involves (depending on system)
  Converting values to a canonical form, serializing objects, copying arguments passed by reference, etc.

## Slide 62: RPC Details (1/3)
Equivalence with regular procedure call
  Parameters Request Message
  Result  Reply message
  Name of Procedure: Passed in request message
  Return Address: mbox2 (client return mail box)
Stub generator: Compiler that generates stubs
  Input: interface definitions in an “interface definition language (IDL)”
    Contains, among other things, types of arguments/return
  Output: stub code in the appropriate source language
    Code for client to pack message, send it off, wait for result, unpack result and return to caller
    Code for server to unpack message, call procedure, pack results, send them off
Notes: …
- You might imagine that this stub code, to marshal arguments and make requests over the network, looks similar for many different remote function calls. We can actually generate it automatically, with a compiler!

## Slide 63: RPC Details (2/3)
Cross-platform issues:
  What if client/server machines are different architectures/ languages?
    Convert everything to/from some canonical form
    Tag every item with an indication of how it is encoded (avoids unnecessary conversions)
How does client know which mbox (destination queue) to send to?
  Need to translate name of remote service into network endpoint (Remote machine, port, possibly other info)
  Binding: the process of converting a user-visible name into a network endpoint
    This is another word for “naming” at network level
    Static: fixed at compile time
    Dynamic: performed at runtime

## Slide 64: RPC Details (3/3)
Dynamic Binding
  Most RPC systems use dynamic binding via name service
    Name service provides dynamic translation of service  mbox
  Why dynamic binding?
    Access control: check who is permitted to access service
    Fail-over: If server fails, use a different one
What if there are multiple servers?
  Could give flexibility at binding time
    Choose unloaded server for each new client
  Could provide same mbox (router level redirect)
    Choose unloaded server for each new request
    Only works if no state carried from one call to next
What if multiple clients?
  Pass pointer to client-specific return mbox in request

## Slide 65: Problems with RPC: Non-Atomic Failures
Different failure modes in dist. system than on a single machine
Consider many different types of failures
  User-level bug causes address space to crash
  Machine failure, kernel bug causes all processes on same machine to fail
  Some machine is compromised by malicious party
Before RPC: whole system would crash/die
After RPC: One machine crashes/compromised while others keep working
Can easily result in inconsistent view of the world
  Did my cached data get written back or not?
  Did server do what I requested or not?
Answer? Distributed transactions/Byzantine Commit

## Slide 66: Problems with RPC: Performance
RPC is not performance transparent:
  Cost of Procedure call « same-machine RPC « network RPC
  Overheads: Marshalling, Stubs, Kernel-Crossing, Communication
Programmers must be aware that RPC is not free
  Caching can help, but may make failure handling complex

## Slide 67: Cross-Domain Communication/Location Transparency
How do address spaces communicate with one another?
  Shared Memory with Semaphores, monitors, etc…
  File System
  Pipes (1-way communication)
  “Remote” procedure call (2-way communication)
RPC’s can be used to communicate between address spaces on different machines or the same machine
  Services can be run wherever it’s most appropriate
  Access to local and remote services looks the same
Examples of RPC systems:
  CORBA (Common Object Request Broker Architecture)
  DCOM (Distributed COM)
  RMI (Java Remote Method Invocation)

## Slide 68: Microkernel operating systems
Example: split kernel into application-level servers.
  File system looks remote, even though on same machine
Why split the OS into separate domains?
  Fault isolation: bugs are more isolated (build a firewall)
  Enforces modularity: allows incremental upgrades of pieces of software (client or server)
  Location transparent: service can be local or remote
    For example in the X windowing system: Each X client can be on a separate machine from X server; Neither has to run on the machine with the frame buffer.
App
App
file system
Windowing
Networking
VM
Threads
App
Monolithic Structure
App
File
sys
windows
RPC
address
spaces
threads
Microkernel Structure

## Slide 69: Network-Attached Storage and the CAP Theorem
Consistency:
  Changes appear to everyone in the same serial order
Availability:
  Can get a result at any time
Partition-Tolerance
  System continues to work even when network becomes partitioned
Consistency, Availability, Partition-Tolerance (CAP) Theorem: Cannot have all three at same time
  Otherwise known as “Brewer’s Theorem”
Network

## Slide 70: Distributed File Systems
Transparent access to files stored on a remote disk
Mount remote files into your local file system
  Directory in local file system refers to remote files
  e.g., /users/jane/prog/foo.c on laptop actually refers to /prog/foo.c on adj.cs.berkeley.edu
Naming Choices:
  [Hostname,localname]: Filename includes server
    No location or migration transparency, except through DNS remapping
  A global name space: Filename unique in “world”
    Can be served by any server
Network
Read File
Data
Server
Client
mount
coeus:/sue
mount
adj:/prog
mount
adj:/jane

## Slide 71: Enabling Design: VFS
The System Call Interface
Process
Management
Memory Management
Filesystems
Device Control
Networking
Architecture
Dependent
Code
Memory Manager
Device Control
Network Subsystem
File System Types
Block Devices
IF drivers
Concurrency, multitasking
Virtual memory
Files and dirs: the VFS
TTYs and device access
Connectivity

## Slide 72: Recall: Layers of I/O…
length = read(input_fd, buffer, BUFFER_SIZE);
ssize_t read(int, void *, size_t) {
marshal args into registers
issue syscall
register result of syscall to rtn value
};
void syscall_handler (struct intr_frame *f) {
unmarshall call#, args from regs
dispatch : handlers[call#](args)
marshal results fo syscall ret
}
Exception UK, interrupt processing
ssize_t vfs_read(struct file *file, char __user *buf, size_t count, loff_t *pos) {
User Process/File System relationship
call device driver to do the work
}
User App:
User library:
Device Driver
High Level I/O
Low Level I/O
Syscall
File System
I/O Driver
Application / Service

## Slide 73: Virtual Filesystem Switch
VFS: Virtual abstraction similar to local file system
  Provides virtual superblocks, inodes, files, etc
  Compatible with a variety of local and remote file systems
    provides object-oriented way of implementing file systems
VFS allows the same system call interface (the API) to be used for different types of file systems
  The API is to the VFS interface, rather than any specific type of file system

## Slide 74: VFS Common File Model in Linux
Four primary object types for VFS:
  superblock object: represents a specific mounted filesystem
  inode object: represents a specific file
  dentry object: represents a directory entry
  file object: represents open file associated with process
There is no specific directory object (VFS treats directories as files)
May need to fit the model by faking it
  Example: make it look like directories are files
  Example: make it look like have inodes, superblocks, etc.

## Slide 75: Simple Distributed File System
Remote Disk: Reads and writes forwarded to server
  Use Remote Procedure Calls (RPC) to translate file system calls into remote requests
  No local caching, but can be cache at server-side
Advantage: Server provides consistent view of file system to multiple clients
Problems? Performance!
  Going over network is slower than going to local memory
  Lots of network traffic/not well pipelined
  Server can be a bottleneck
Server
Read (RPC)
Return (Data)
Write (RPC)
ACK
cache
Client
Client

## Slide 76: Use of caching to reduce network load
Client
cache
F1:V1
F1:V2
Read (RPC)
Return (Data)
Write (RPC)
ACK
cache
cache
Idea: Use caching to reduce network load
  In practice: use buffer cache at source and destination
Advantage: if open/read/write/close can be done locally, don’t need to do any network traffic…fast!
Problems:
  Failure:
    Client caches have data not committed at server
  Cache consistency!
    Client caches not consistent with server/each other
F1:V1
F1:V2
read(f1)
write(f1)
V1
read(f1)V1
read(f1)V1
OK
read(f1)V1
read(f1)V2
Crash!
Crash!
Server
Client

## Slide 77: Dealing with Failures
What if server crashes? Can client wait until it comes back and just continue making requests?
  Changes in server's cache but not in disk are lost
What if there is shared state across RPC's?
  Client opens file, then does a seek
  Server crashes
  What if client wants to do another read?
Similar problem: What if client removes a file but server crashes before acknowledgement?

## Slide 78: Stateless Protocol
Stateless Protocol: A protocol in which all information required to service a request is included with the request
Even better: Idempotent Operations – repeating an operation multiple times is same as executing it just once (e.g., storing to a mem addr.)
Client: timeout expires without reply, just run the operation again (safe regardless of first attempt)
Recall HTTP: Also a stateless protocol
  Include cookies with request to simulate a session

## Slide 79: Case Study: Network File System (NFS)
Three Layers for NFS system
  UNIX file-system interface: open, read, write, close calls + file descriptors
  VFS layer: distinguishes local from remote files
    Calls the NFS protocol procedures for remote requests
  NFS service layer: bottom layer of the architecture
    Implements the NFS protocol
NFS Protocol: RPC for file operations on server
  XDR Serialization standard for data format independence
  Reading/searching a directory
  manipulating links and directories
  accessing file attributes/reading and writing files
Write-through caching: Modified data committed to server’s disk before results are returned to the client
  lose some of the advantages of caching
  time to perform write() can be long
  Need some mechanism for readers to eventually notice changes! (more on this later)

## Slide 80: NFS Continued
NFS servers are stateless; each request provides all arguments require for execution
  E.g. reads include information for entire operation, such as ReadAt(inumber,position), not Read(openfile)
  No need to perform network open() or close() on file – each operation stands on its own
Idempotent: Performing requests multiple times has same effect as performing them exactly once
  Example: Server crashes between disk I/O and message send, client resend read, server does operation again
  Example: Read and write file blocks: just re-read or re-write file block – no other side effects
  Example: What about “remove”? NFS does operation twice and second time returns an advisory error
Failure Model: Transparent to client system
  Is this a good idea? What if you are in the middle of reading a file and server crashes?
  Options (NFS Provides both):
    Hang until server comes back up (next week?)
    Return an error. (Of course, most applications don’t know they are talking over network)

## Slide 81: NFS Architecture

## Slide 82: NFS Cache consistency
NFS protocol: weak consistency
  Client polls server periodically to check for changes
    Polls server if data hasn’t been checked in last 3-30 seconds (exact timeout it tunable parameter).
    Thus, when file is changed on one client, server is notified, but other clients use old version of file until timeout.
  What if multiple clients write to same file?
    In NFS, can get either version (or parts of both)
    Completely arbitrary!
cache
F1:V2
Write (RPC)
ACK
cache
cache
F1:V1
F1:V2
Client
Server
Client
F1:V2
F1 still ok?
No: (F1:V2)

## Slide 83: Sequential Ordering Constraints
What sort of cache coherence might we expect?
  i.e. what if one CPU changes file, and before it’s done, another CPU reads file?
Example: Start with file contents = “A”
What would we actually want?
  Assume we want distributed system to behave exactly the same as if all processes are running on single system
    If read finishes before write starts, get old copy
    If read starts after write finishes, get new copy
    Otherwise, get either new or old copy
  For NFS:
    If read starts more than 30 seconds after write, get new copy; otherwise, could get partial update
Read: gets A
Read: gets A or B
Write B
Write C
Read: parts of B or C
Client 1:
Client 2:
Client 3:
Read: parts of B or C
Time

## Slide 84: NFS Pros and Cons
NFS Pros:
  Simple, Highly portable
NFS Cons:
  Sometimes inconsistent!
  Doesn’t scale to large # clients
    Must keep checking to see if caches out of date
    Server becomes bottleneck due to polling traffic

## Slide 85: Andrew File System
Andrew File System (AFS, late 80’s)  DCE DFS (commercial product)
Callbacks: Server records who has copy of file
  On changes, server immediately tells all with old copy
  No polling bandwidth (continuous checking) needed
Write through on close
  Changes not propagated to server until close()
  Session semantics: updates visible to other clients only after the file is closed
    As a result, do not get partial writes: all or nothing!
    Although, for processes on local machine, updates visible immediately to other programs who have file open
In AFS, everyone who has file open sees old version
  Don’t get newer versions until reopen file

## Slide 86: Andrew File System (con’t)
Data cached on local disk of client as well as memory
  On open with a cache miss (file not on local disk):
    Get file from server, set up callback with server
  On write followed by close:
    Send copy to server; tells all clients with copies to fetch new version from server on next open (using callbacks)
What if server crashes? Lose all callback state!
  Reconstruct callback information from client: go ask everyone “who has which files cached?”
AFS Pro: Relative to NFS, less server load:
  Disk as cache  more files can be cached locally
  Callbacks  server not involved if file is read-only
For both AFS and NFS: central server is bottleneck!
  Performance: all writesserver, cache missesserver
  Availability: Server is single point of failure
  Cost: server machine’s high cost relative to workstation

## Slide 87: Summary (1/2)
TCP: Reliable byte stream between two processes on different machines over Internet (read, write, flush)
  Uses window-based acknowledgement protocol
  Congestion-avoidance dynamically adapts sender window to account for congestion in network
Remote Procedure Call (RPC): Call procedure on remote machine or in remote domain
  Provides same interface as procedure
  Automatic packing and unpacking of arguments without user programming (in stub)
  Adapts automatically to different hardware and software architectures at remote end

## Slide 88: Summary (2/2)
Distributed File System:
  Transparent access to files stored on a remote disk
  Caching for performance
VFS: Virtual File System layer (Or Virtual Filesystem Switch)
  Provides mechanism which gives same system call interface for different types of file systems
Cache Consistency: Keeping client caches consistent with one another
  If multiple clients, some reading and some writing, how do stale cached copies get updated?
  NFS: check periodically for changes
  AFS: clients register callbacks to be notified by server of changes