## Slide 1: CS162 Operating Systems and Systems Programming Lecture 21 Filesystems 1: Performance, Queueing Theory, Filesystem Design
April 6th, 2023
Prof. John Kubiatowicz
http://cs162.eecs.Berkeley.edu

## Slide 2: Recall: Magnetic Disks
Cylinders: all the tracks under the head at a given point on all surfaces
Read/write data is a three-stage process:
  Seek time: position the head/arm over the proper track
  Rotational latency: wait for desired sector to rotate under r/w head
  Transfer time: transfer a block of bits (sector) under r/w head
Sector
Track
Cylinder
Head
Platter
Software
Queue
(Device Driver)
Hardware
Controller
Media Time
(Seek+Rot+Xfer)
Request
Result
Disk Latency = Queueing Time + Controller time +
Seek Time + Rotation Time + Xfer Time

## Slide 3: Recall: FLASH Memory
Like a normal transistor but:
  Has a floating gate that can hold charge
  To write: raise or lower wordline high enough to cause charges to tunnel
  To read: turn on wordline as if normal transistor
    presence of charge changes threshold and thus measured current
Two varieties:
  NAND: denser, must be read and written in blocks
  NOR: much less dense, fast to read and write
V-NAND: 3D stacking (Samsung claims 1TB possible in 1 chip)
Samsung 2015:
512GB, NAND Flash

## Slide 4: Ways of Measuring Performance: Times (s) and Rates (op/s)
Latency – time to complete a task
  Measured in units of time (s, ms, us, …, hours, years)
Response Time - time to initiate and operation and get its response
  Able to issue one that depends on the result
  Know that it is done (anti-dependence, resource usage)
Throughput or Bandwidth – rate at which tasks are performed
  Measured in units of things per unit time (ops/s, GFLOP/s)
Start up or “Overhead” – time to initiate an operation
Most I/O operations are roughly linear in b bytes
  Latency(b) = Overhead + b/TransferCapacity
Performance???
  Operation time (4 mins to run a mile…)
  Rate (mph, mpg, …)

## Slide 5: Example: Overhead in Fast Network
Consider a link () with startup cost
Latency:
Effective Bandwidth:
Half-power Bandwidth:
For this example, half-power bandwidth occurs at x
Length (x)

## Slide 6: Example: 10 ms Startup Cost (e.g., Disk)
Half-power bandwidth at
Large startup cost can degrade effective bandwidth
Amortize it by performing I/O in larger blocks
  Half-power x = 1,250,000 bytes!
Length (x)

## Slide 7: What Determines Peak BW for I/O?
Bus Speed
  PCI-X: 1064 MB/s = 133 MHz x 64 bit (per lane)
  ULTRA WIDE SCSI: 40 MB/s
  Serial Attached SCSI & Serial ATA & IEEE 1394 (firewire): 1.6 Gb/s full duplex (200 MB/s)
  USB 3.0 – 5 Gb/s
  Thunderbolt 3 – 40 Gb/s
Device Transfer Bandwidth
  Rotational speed of disk
  Write / Read rate of NAND flash
  Signaling rate of network link
Whatever is the bottleneck in the path…

## Slide 8: Sequential Server Performance
Single sequential “server” that can deliver a task in time operates at rate (on average, in steady state, …)
  →
  →
Applies to a processor, a disk drive, a person, a TA, …
L
L
L
L
…
time
L

## Slide 9: Single Pipelined Server
Single pipelined server of stages for tasks of length (i.e., time per stage) delivers at rate .
  , →
  , →
L
…
L
L
L
L
L
L
L
L
logical operation
divided over distinct resources
time

## Slide 10: Example Systems “Pipelines”
Anything with queues between operational process behaves roughly “pipeline like”
Important difference is that “initiations” are decoupled from processing
  May have to queue up a burst of operations
  Not synchronous and deterministic like in 61C
User Process
syscall
File
System
Upper Driver
Lower Driver
I/O Processing
Communication

## Slide 11: Multiple Servers
servers handling tasks of length delivers at rate .
  , →
  , →
In 61C you saw multiple processors (cores)
  Systems present lots of multiple parallel servers
  Often with lots of queues
L
…
k

## Slide 12: Example Systems “Parallelism”
User Process
syscall
File
System
Upper Driver
Lower Driver
I/O Processing
Communication
User Process
User Process
Parallel Computation, Databases, …

## Slide 13: I/O Performance
Response Time = Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
Performance of I/O subsystem
  Metrics: Response Time, Throughput
  Effective BW per op = transfer size / response time
    EffBW(n) = n / (S + n/B) = B / (1 + SB/n )
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%
# of ops
Fixed overhead
time per op

## Slide 14: I/O Performance
Response Time = Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
Performance of I/O subsystem
  Metrics: Response Time, Throughput
  Effective BW per op = transfer size / response time
    EffBW(n) = n / (S + n/B) = B / (1 + SB/n )
  Contributing factors to latency:
    Software paths (can be loosely modeled by a queue)
    Hardware controller
    I/O device service time
Queuing behavior:
  Can lead to big increases of latency as utilization increases
  Solutions?
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%

## Slide 15: A Simple Deterministic World
Assume requests arrive at regular intervals, take a fixed time to process, with plenty of time between …
Service rate (μ = 1/TS) - operations per second
Arrival rate: (λ = 1/TA) - requests per second
Utilization: U = λ/μ , where λ < μ
Average rate is the complete story
Queue
Server
arrivals
departures
TQ
TS
TA
TA
TA
TS
Tq

## Slide 16: A Ideal Linear World
What does the queue wait time look like?
  Grows unbounded at a rate ~ (Ts/TA) till request rate subsides
Offered Load (TS/TA)
Delivered Throughput
0
1
1
time
Queue delay
Delivered Throughput
0
1
1
Offered Load (TS/TA)
Empty Queue
Saturation
Unbounded
time
Queue delay

## Slide 17: A Bursty World
Requests arrive in a burst, must queue up till served
Same average arrival time, but almost all of the requests experience large queue delays
Even though average utilization is low
Queue
Server
arrivals
departures
TQ
TS
Q depth
Server
Arrivals

## Slide 18: So how do we model the burstiness of arrival?
Elegant mathematical framework if you start with exponential distribution
  Probability density function of a continuous random variable with a mean of 1/λ
  f(x) = λe-λx
  “Memoryless”
Chart: 
| 1E-3 | 0.01 | 0.02 | 0.04 | 0.08 | 0.16 | 0.32 | 0.64 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 10
f(x) | 0.999 | 0.99005 | 0.9802 | 0.96079 | 0.92312 | 0.85214 | 0.72615 | 0.52729 | 0.36788 | 0.13534 | 0.049787 | 0.018316 | 0.0067379 | 0.0024788 | 0.00091188 | 0.00033546 | 4.54e-05
Likelihood of an event occurring is independent of how long we’ve been waiting
Lots of short arrival intervals (i.e., high instantaneous rate)
Few long gaps (i.e., low instantaneous rate)
x (λ)
mean arrival interval (1/λ)

## Slide 19: Background: General Use of Random Distributions
Server spends variable time (T) with customers
  Mean (Average) m = p(T)T
  Variance (stddev2) 2 = p(T)(T-m)2 = p(T)T2-m2
  Squared coefficient of variance: C = 2/m2 Aggregate description of the distribution
Important values of C:
  No variance or deterministic  C=0
  “Memoryless” or exponential  C=1
    Past tells nothing about future
    Poisson process – purely or completely random process
    Many complex systems (or aggregates) are well described as memoryless
  Disk response times C  1.5 (majority seeks < average)
Mean
(m)
mean
Memoryless
Distribution
of service times


## Slide 20: Introduction to Queuing Theory
Departures
Arrivals
Queuing System
What about queuing time??
  Let’s apply some queuing theory
  Queuing Theory applies to long term, steady state behavior  Arrival rate = Departure rate
Arrivals characterized by some probabilistic distribution
Departures characterized by some probabilistic distribution
Queue
Controller
Disk
Notes: Old and New Testament by Kleirock
Regret skipping as grad student

## Slide 21: Little’s Law
In any stable system
  Average arrival rate = Average departure rate
The average number of jobs/tasks in the system (N) is equal to arrival time / throughput (λ) times the response time (L)
  N (jobs) = λ (jobs/s) x L (s)
Regardless of structure, bursts of requests, variation in service
  Instantaneous variations, but it washes out in the average
  Overall, requests match departures
arrivals
departures
N
λ
L

## Slide 22: Example
λ = 1
L = 5
0
1
2
3
4
5
6
7
8
16
9
10
11
12
13
14
15
time
Jobs
L = 5
N = 5 jobs
A: N = λ x L
E.g., N = λ x L = 5

## Slide 23: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
Job i
L(1)

## Slide 24: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
What is the system occupancy, i.e., average
number of jobs in the system?
Job i

## Slide 25: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
S(i) = L(i) * 1 = L(i)
Job i
S(1)
S(2)
S = S(1) + S(2) + … + S(k) = L(1) + L(2) + … + L(k)
S(k)

## Slide 26: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
S(i) = L(i) * 1 = L(i)
Average occupancy (Navg) = S/T
Job i
S= area

## Slide 27: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
S(i) = L(i) * 1 = L(i)
Job i
S(1)
S(2)
Navg = S/T = (L(1) + … + L(k))/T
S(k)

## Slide 28: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
S(i) = L(i) * 1 = L(i)
Job i
S(1)
S(2)
Navg = (L(1) + … + L(k))/T = (Ntotal/T)*(L(1) + … + L(k))/Ntotal
S(k)

## Slide 29: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
S(i) = L(i) * 1 = L(i)
Job i
S(1)
S(2)
Navg = (Ntotal/T)*(L(1) + … + L(k))/Ntotal = λavg × Lavg
S(k)

## Slide 30: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
S(i) = L(i) * 1 = L(i)
Job i
S(1)
S(2)
Navg = λavg × Lavg
S(k)

## Slide 31: Little’s Law Applied to a Queue
When Little’s Law applied to a queue, we get:
Average length of the queue
Average Arrival Rate
Average time “waiting” in queue

## Slide 32: A Little Queuing Theory: Computing TQ
Assumptions:
  System in equilibrium; No limit to the queue
  Time between successive arrivals is random and memoryless
Parameters that describe our system:
  : mean number of arriving customers/second
  Tser: mean time to service a customer (“m1”)
  C: squared coefficient of variance = 2/m12
  μ: service rate = 1/Tser
  u: server utilization (0u1): u = /μ =   Tser
Results:
  Memoryless service distribution (C = 1): (an “M/M/1 queue”):
    Tq = Tser x u/(1 – u)
  General service distribution, 1 server (an “M/G/1 queue”):
    Tq = Tser x ½(1+C) x u/(1 – u)
Arrival Rate

Queue
Server
Service Rate
μ=1/Tser
Why does response/queueing delay grow unboundedly even though the utilization is < 1 ?
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%

## Slide 33: System Performance In presence of a Queue
Request Rate ( ) - “offered load”
Service Rate () - “delivered load”
Latency ()
Operation Time
Time
“Half-Power Point” : load at which system delivers half of peak performance
Design and provision systems to operate roughly in this regime
Latency low and predictable, utilization good: ~50%
,
Why does latency blow up as we approach 100% utilization?
  Queue builds up on each burst
  But very rarely (or never) gets a chance to drain

## Slide 34: Why unbounded response time?
Assume deterministic arrival process and service time
  Possible to sustain utilization = 1 with bounded response time!
time
arrival time
service time

## Slide 35: Why unbounded response time?
Assume stochastic arrival process (and service time)
  No longer possible to achieve utilization = 1
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%
time
This wasted time can never be reclaimed! So cannot achieve u = 1!

## Slide 36: A Little Queuing Theory: An Example
Example Usage Statistics:
  User requests 10 x 8KB disk I/Os per second
  Requests & service exponentially distributed (C=1.0)
  Avg. service = 20 ms (From controller+seek+rot+trans)
Questions:
  How utilized is the disk?
    Ans: server utilization, u = Tser
  What is the average time spent in the queue?
    Ans: Tq
  What is the number of requests in the queue?
    Ans: Lq
  What is the avg response time for disk request?
    Ans: Tsys = Tq + Tser
Computation:
 (avg # arriving customers/s) = 10/s
Tser (avg time to service customer) = 20 ms (0.02s)
u (server utilization) =  x Tser= 10/s x .02s = 0.2
Tq (avg time/customer in queue) = Tser x u/(1 – u) = 20 x 0.2/(1-0.2) = 20 x 0.25 = 5 ms (0 .005s)
Lq (avg length of queue) =  x Tq=10/s x .005s = 0.05
Tsys (avg time/customer in system) =Tq + Tser= 25 ms

## Slide 37: Queuing Theory Resources
Resources page contains Queueing Theory Resources (under Readings):
  Scanned pages from Patterson and Hennessy book that gives further discussion and simple proof for general equation: https://cs162.eecs.berkeley.edu/static/readings/patterson_queue.pdf
  A complete website full of resources: http://web2.uwindsor.ca/math/hlynka/qonline.html
Some previous midterms with queueing theory questions
Assume that Queueing Theory is fair game for Midterm III!

## Slide 38: Optimize I/O Performance
How to improve performance?
  Make everything faster 
  More Decoupled (Parallelism) systems
    multiple independent buses or controllers
  Optimize the bottleneck to increase service rate
    Use the queue to optimize the service
  Do other useful work while waiting
Queues absorb bursts and smooth the flow
Admissions control (finite queues)
  Limits delays, but may introduce unfairness and livelock
Response Time = Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%

## Slide 39: Recall: I/O and Storage Layers
High Level I/O
Low Level I/O
Syscall
File System
I/O Driver
Application / Service
Streams
File Descriptors
open(), read(), write(), close(), …
Files/Directories/Indexes
Commands and Data Transfers
Disks, Flash, Controllers, DMA
What we covered in Lecture 4
Open File Descriptions
What we just covered…
What we will cover next…

## Slide 40: From Storage to File Systems
I/O API and
syscalls
Variable-Size Buffer
File System
Block
Logical Index, Typically 4 KB
Hardware Devices
Memory Address
HDD
Sector(s)
Physical Index,
512B or 4KB
SSD
Flash Trans. Layer
Phys. Block
Phys Index., 4KB
Sector(s)
Sector(s)
Erasure Page

## Slide 41: Building a File System
File System: Layer of OS that transforms block interface of disks (or other block devices) into Files, Directories, etc.
Classic OS situation: Take limited hardware interface (array of blocks) and provide a more convenient/useful interface with:
  Naming: Find file by name, not block numbers
  Organize file names with directories
  Organization: Map files to blocks
  Protection: Enforce access restrictions
  Reliability: Keep files intact despite crashes, hardware failures, etc.

## Slide 42: Recall: User vs. System View of a File
User’s view:
  Durable Data Structures
System’s view (system call interface):
  Collection of Bytes (UNIX)
  Doesn’t matter to system what kind of data structures you want to store on disk!
System’s view (inside OS):
  Collection of blocks (a block is a logical transfer unit, while a sector is the physical transfer unit)
  Block size  sector size; in UNIX, block size is 4KB

## Slide 43: Translation from User to System View
What happens if user says: “give me bytes 2 – 12?”
  Fetch block corresponding to those bytes
  Return just the correct portion of the block
What about writing bytes 2 – 12?
  Fetch block, modify relevant portion, write out block
Everything inside file system is in terms of whole-size blocks
  Actual disk I/O happens in blocks
  read/write smaller than block size needs to translate and buffer
File
System
File (Bytes)

## Slide 44: Disk Management
Basic entities on a disk:
  File: user-visible group of blocks arranged sequentially in logical space
  Directory: user-visible index mapping names to files
The disk is accessed as linear array of sectors
How to identify a sector?
  Physical position
    Sectors is a vector [cylinder, surface, sector]
    Not used anymore
    OS/BIOS must deal with bad sectors
  Logical Block Addressing (LBA)
    Every sector has integer address
    Controller translates from address  physical position
    Shields OS from structure of disk

## Slide 45: What Does the File System Need?
Track free disk blocks
  Need to know where to put newly written data
Track which blocks contain data for which files
  Need to know where to read a file from
Track files in a directory
  Find list of file's blocks given its name
Where do we maintain all of this?
  Somewhere on disk

## Slide 46: Data Structures on Disk
Somewhat different from data structures in memory
Access a block at a time
  Can't efficiently read/write a single word
  Have to read/write full block containing it
  Ideally want sequential access patterns
Durability
  Ideally, file system is in meaningful state upon shutdown
  This obviously isn't always the case…

## Slide 47: File System Design

## Slide 48: Critical Factors in File System Design
(Hard) Disks Performance !!!
  Maximize sequential access, minimize seeks
Open before Read/Write
  Can perform protection checks and look up where the actual file resource are, in advance
Size is determined as they are used !!!
  Can write (or read zeros) to expand the file
  Start small and grow, need to make room
Organized into directories
  What data structure (on disk) for that?
Need to carefully allocate / free blocks
  Such that access remains efficient

## Slide 49: Components of a File System
File path
Directory
Structure
File
Header
Structure
File number
“inumber”
…
Data blocks
“inode”
One Block = multiple sectors
Ex: 512 sector, 4K block

## Slide 50: Example of BSD/Linux-like Inode structure
Sample file in multilevel indexed format:
  Data Stored in Blocks
  10 direct ptrs, 1K blocks
  One Indirect block
  One Doubly-indirect Block
  One Triply-indirect Block
Example accesses
  How many accesses for block #23? (assume file header accessed on open)?
    Two: One for indirect block, one for data
  How about block #5?
    One: One for data
  Block #340?
    Three: double indirect block, indirect block, and data

## Slide 51: Recall: Abstract Representation of a Process
Suppose that we execute
open(“foo.txt”)
and that the result is 3
Next, suppose that we execute
read(3, buf, 100)
and that the result is 100
User Space
Kernel Space
Address Space (Memory)
Thread’s Regs
File Descriptors
Not shown: Initially contains 0, 1, and 2 (stdin, stdout, stderr)
3
File: foo.txt
Position: 100
Open File Description
Process
…

## Slide 52: Components of a File System
Open file description is better described as remembering the inumber (file number) of the file, not its name
User Space
Kernel Space
Address Space (Memory)
Thread’s Regs
File Descriptors
Not shown: Initially contains 0, 1, and 2 (stdin, stdout, stderr)
3
File: foo.txt inumber
Position: 100
Open File Description
Process
…

## Slide 53: Components of a File System
Open performs Name Resolution
  Translates path name into a “file number”
Read and Write operate on the file number
  Use file number as an “index” to locate the blocks
4 components:
  directory, index structure, storage blocks, free space map
file name
offset
directory structure
file number
offset
index structure (“inode”)
storage block

## Slide 54: How to get the File Number?
Look up in directory structure
A directory is a file containing <file_name : file_number> mappings
  File number could be a file or another directory
  Operating system stores the mapping in the directory in a format it interprets
  Each <file_name : file_number> mapping is called a directory entry
Process isn’t allowed to read the raw bytes of a directory
  The read function doesn’t work on a directory
  Instead, see readdir, which iterates over the map without revealing the raw bytes
Why shouldn’t the OS let processes read/write the bytes of a directory?

## Slide 55: Directories

## Slide 56: Directory Abstraction
Directories are specialized files
  Contents: List of pairs <file name, file number>
System calls to access directories
  open / creat / readdir traverse the structure
  mkdir / rmdir add/remove entries
  link / unlink (rm)
libc support
  DIR * opendir (const char *dirname)
  struct dirent * readdir (DIR *dirstream)
  int readdir_r (DIR *dirstream, struct dirent *entry, struct dirent **result)
/usr
/usr/lib4.3
/usr/lib4.3/foo
/usr/lib

## Slide 57: Directory Structure
How many disk accesses to resolve “/my/book/count”?
  Read in file header for root (fixed spot on disk)
  Read in first data block for root
    Table of file name/index pairs.
    Search linearly – ok since directories typically very small
  Read in file header for “my”
  Read in first data block for “my”; search for “book”
  Read in file header for “book”
  Read in first data block for “book”; search for “count”
  Read in file header for “count”
Current working directory: Per-address-space pointer to a directory used for resolving file names
  Allows user to specify relative filename instead of absolute path (say CWD=“/my/book” can resolve “count”)

## Slide 58: In-Memory File System Structures
Open syscall: find inode on disk from pathname (traversing directories)
  Create “in-memory inode” in system-wide open file table
  One entry in this table no matter how many instances of the file are open
Read/write syscalls look up in-memory inode using the file handle
(fd)
fd
inode

## Slide 59: Characteristics of Files
Published in FAST 2007

## Slide 60: Observation #1: Most Files Are Small

## Slide 61: Observation #2: Most Bytes are in Large Files

## Slide 62: Conclusion
Bursts & High Utilization introduce queuing delays
Queuing Latency:
  M/M/1 and M/G/1 queues: simplest to analyze
  As utilization approaches 100%, latency  
  Tq = Tser x ½(1+C) x u/(1 – u))
File System:
  Transforms blocks into Files and Directories
  Optimize for access and usage patterns
  Maximize sequential access, allow efficient random access
File (and directory) defined by header, called “inode”
Naming: translating from user-visible names to actual sys resources
  Directories used for naming for local file systems
  Linked or tree structure stored in files